## Slide 1: 求解组合优化问题的光学实现
报告人：樊泽洋

## Slide 2: 背景知识
我们希望某一个算法时间复杂度越低越好
算法复杂度：O(1)、O(n)、O(nc)……
比多项式时间O(nc)更慢是不能接受的
O(n!)，n=100时，100!≈9.3*10157, 远大于宇宙中原子总数
Notes: 计算复杂性理论是一门研究有限的计算资源如何影响计算性能的一门学科，它的理论框架常伴随着组合优化问题和复杂的约束条件。
最被广泛关注的计算资源是“时间”和“空间”，也就是说，我们关注的是“给定的计算问题是否在一段较短的时间内被解决”。
横轴代表输入的大小，纵坐标表示消耗的时间

## Slide 3: 千禧年大奖难题之首 P=NP?
P：Polynomial-time
能够在多项式时间内用算法求解的问题
NP：Nondeterministic polynomial-time
不确定是否在多项式时间求解，但可以在多项式时间内验证的问题
NP-Complete：
所有NP问题都可以规约到某一NP问题
NP-Hard：
所有NP问题都可以规约到某一问题
Notes: NPC问题还是属于NP问题，NPC问题就是大量NP问题经过规约后发现的终极bossNP问题。
P=NP？问题不仅是一个数学问题，它对现实有着十分重要的指导意义，这些问题的答案让我们知道计算机可以解决哪些问题、不可以解决哪些问题。

## Slide 4: Ising 模型（NP-Hard）
伊辛模型是统计物理中的一个基本模型，广泛用于描述具有相互作用的体系。
每个分子都有自旋，记为σ ( σ={+1,-1} )
临近的两个分子之间存在相互作用Jij
系统中可能存在外场，记为 b
系统的Hamilton量（可以看作能量）：
当耦合矩阵J、外场b稳定时，Ising模型自旋分布σ趋于能量最小。该问题被证明为NP-Hard问题。
…… 无穷维
Notes: 伊辛模型的提出是为了解释铁磁物质的相变，即磁铁在加热到一定临界温度以上会出现磁性消失的现象，而降温到临界温度以下又会表现出磁性。这种有磁性、无磁性两相之间的转变，是一种连续相变（也叫二级相变）。
伊辛模型假设铁磁物质是由一堆规则排列的小磁针构成，每个磁针只有上下两个方向（自旋）。相邻的小磁针之间通过能量约束发生相互作用，同时又会由于环境热噪声的干扰而发生磁性的随机转变。
涨落的大小由关键的温度参数决定，温度越高，随机涨落干扰越强，如果温度很低，则小磁针相对宁静。
我们定义伊辛模型Hamilton量的最小值为该模型的基态。

## Slide 5: 一些NP问题与伊辛模型的关系
最大割问题：给定无向图G(V,E)，wij为顶点i j边的权，上求解一种分割方法将顶点集分为2类，使得其连接边集最大。
数集等分问题：给定N个元素的数值集合S={m1,m2……mN}，将集合S分成两部分，使两个集合数值之和相等或差异最小。
许多NPC和NPhard问题可以转化为伊辛模型
Lucas A. Ising formulations of many NP problems[J]. Frontiers in physics, 2014, 2: 5.
Notes: 无向图G(V，E)，V是其顶点集，E是其边集。

## Slide 6: 启发式算法求解伊辛模型
Metropolis Hastings算法
满足细致平稳条件
模拟退火算法
随着代数的增加降低温度T
有效逃离了局部最优，但计算量较大
马尔可夫过程
Notes: 对与Metropolis算法，首先初始化一个自旋配置，每翻转一个自旋分布，并以Metropolis准则去接受它，可以证明该接受准则满足细致平稳条件，故该马尔可夫过程最终稳定状态服从吉布斯分布。
Metropolis准则是模拟退火算法的基础，通过逐步降低温度T，使得对能量差大于0的接受概率逐步降低，稳定到全局最优。

## Slide 7: 离散Hopfield网络求解Ising模型
local minima
离散的Hopfield网络（1982 by Hopfield）是一个二值单层全反馈神经网络，其结构关系为：
网络能量函数定义为：
若系统按照异步工作方式，权重矩阵为对称阵，网络最终会快速收敛到一个吸引子，并且系统能量单调递减：
只会“下山”
不会“爬山”
结合SA与Hopfield
Hopfield J J. Neural networks and physical systems with emergent collective computational abilities[J]. Proceedings of the national academy of sciences, 1982, 79(8): 2554-2558.
Notes: 随着循环代数的增加，DHNN网络能量单调递减的特性，导致DHNN网络只会“下山”不会“爬山”，极易陷入局部最小值，因此单独的离散hopfield网络找到系统真正基态的概率较低。

## Slide 8: DHNN结合退火思想的电子求解伊辛模型
引入逐渐降低的噪声（退火思想）
Cai, Fuxi, et al. "Power-efficient combinatorial optimization using intrinsic noise in memristor Hopfield neural networks." Nature Electronics 3.7 (2020): 409-418.

## Slide 9: Hopfield与Hopfield-SA效果比较
Ground state
问题：
Hopfield-SA流程图：

## Slide 10: DOPO相干光子伊辛机
人工自旋：锁模激光器 Degenerated optical parametric oscillators(DOPO) (相位 0 or π)
测量与反馈回路：产生自旋间耦合，生成伊辛模型
OPO振荡分叉点：
在阈值下：压缩、量子状态
在阈值上：相干（经典）振荡 0 or π
Inagaki T, Haribara Y, Igarashi K, et al. A coherent Ising machine for 2000-node optimization problems[J]. Science, 2016, 354(6312): 603-606.
高达2000自旋
毫秒量级运算

## Slide 11: 空间光学伊辛机
自由度 O(N) instead of O(N2)
Coupling：幅度型SLM
Spin：纯相位型SLM
透镜前：
透镜后光电探测器：
Pierangeli D, Marcucci G, Conti C. Large-scale photonic Ising machine by spatial light modulation[J]. Physical review letters, 2019, 122(21): 213902.

## Slide 12: 空间光学伊辛机-绝热演化
线性的演化模型：
Pierangeli D, Marcucci G, Conti C. Adiabatic evolution on a spatial-photonic Ising machine[J]. Optica, 2020, 7(11): 1535-1543.

## Slide 13: 空间光学伊辛机-规范变换
出发点：两个SLM之间像素对齐误差
对于Mattis自旋玻璃模型：
有规范变换：
相互作用强度的不均匀性被转移到自旋中：
幅度调制
相位调制
相位调制
方轶圣. 面向光学模拟计算的空间微分器和光学伊辛模型[D].浙江大学,2020.
Y.Fang et al., Phys.Rev.Lett (in press)

## Slide 14: 光子循环伊辛采样（PRIS）算法
光子系统的哈密顿量：
ϕ大噪声近似
Ising模型：
对称权重，特征值分解：
线性光子域：
Roques-Carmes C, Shen Y, Zanoci C, et al. Heuristic recurrent algorithms for photonic Ising machines[J]. Nature communications, 2020, 11(1): 1-8.
PRIS运作机制：
构造等效哈密顿系统 近似解

## Slide 15: PRIS实验实施
由13个MZI阵列组成的4自旋系统
芯片酉保真度92%
用第5通道作零差检测
酉矩阵直接映射在芯片上
两个酉矩阵U和U⸷，每个酉矩阵对应两个零差检测矩阵h1和h2，每次迭代执行4次乘法，零差检测算法重建幅度-相位信息：
Prabhu M, Roques-Carmes C, Shen Y, et al. Accelerating recurrent Ising machines in photonic integrated circuits[J]. Optica, 2020, 7(5): 551-558.

## Slide 16: References：
Lucas A. Ising formulations of many NP problems[J]. Frontiers in physics, 2014, 2: 5.
Hopfield J J. Neural networks and physical systems with emergent collective computational abilities[J]. Proceedings of the national academy of sciences, 1982, 79(8): 2554-2558.
Hopfield J J. Neurons with graded response have collective computational properties like those of two-state neurons[J]. Proceedings of the national academy of sciences, 1984, 81(10): 3088-3092.Cui, T. J., Qi, M. Q., Wan, X., Zhao, J., & Cheng, Q. (2014). Coding metamaterials, digital metamaterials and programmable metamaterials. Light: Science & Applications, 3(10), e218-e218.
Zhang, L., Liu, S., Li, L., & Cui, T. J. (2017). Spin-controlled multiple pencil beams and vortex beams with different polarizations generated by Pancharatnam-Berry coding metasurfaces. ACS applied materials & interfaces, 9(41), 36447-36455.
Inagaki T, Haribara Y, Igarashi K, et al. A coherent Ising machine for 2000-node optimization problems[J]. Science, 2016, 354(6312): 603-606.Ding, X., Monticone, F., Zhang, K., Zhang, L., Gao, D., Burokur, S. N., . . . Alù, A. (2015). Ultrathin Pancharatnam–Berry metasurface with maximal cross‐polarization efficiency. Advanced Materials, 27(7), 1195-1200.
McMahon P L, Marandi A, Haribara Y, et al. A fully programmable 100-spin coherent Ising machine with all-to-all connections[J]. Science, 2016, 354(6312): 614-617.Wong, A. M., & Eleftheriades, G. V. (2018). Perfect anomalous reflection with a bipartite Huygens’ metasurface. Physical Review X, 8(1), 011036.
Cen Q, Hao T, Ding H, et al. Microwave photonic ising machine[J]. arXiv preprint arXiv:2011.00064, 2020.
Pierangeli D, Marcucci G, Conti C. Large-scale photonic Ising machine by spatial light modulation[J]. Physical review letters, 2019, 122(21): 213902.
Pierangeli D, Marcucci G, Conti C. Adiabatic evolution on a spatial-photonic Ising machine[J]. Optica, 2020, 7(11): 1535-1543.
Pierangeli D, Rafayelyan M, Conti C, et al. Scalable spin-glass optical simulator[J]. Physical Review Applied, 2021, 15(3): 034087.
Pierangeli D, Marcucci G, Brunner D, et al. Noise-enhanced spatial-photonic Ising machine[J]. Nanophotonics, 2020, 9(13): 4109-4116.
Roques-Carmes C, Shen Y, Zanoci C, et al. Heuristic recurrent algorithms for photonic Ising machines[J]. Nature communications, 2020, 11(1): 1-8.
Prabhu M, Roques-Carmes C, Shen Y, et al. Accelerating recurrent Ising machines in photonic integrated circuits[J]. Optica, 2020, 7(5): 551-558.
Peretto P. Collective properties of neural networks: a statistical physics approach[J]. Biological cybernetics, 1984, 50(1): 51-62.
Cai, Fuxi, et al. "Power-efficient combinatorial optimization using intrinsic noise in memristor Hopfield neural networks." Nature Electronics 3.7 (2020): 409-418.

## Slide 17
谢谢大家聆听！